Type CMG-3ESP Manufacturer Guralp Systems Limited Address 3 Midas House, Calleva Park, Aldermaston, Reading RG7 8EA, UK Phone ++44 118 9819056 E-mail sales@guralp.com Homepage www.guralp.com Category Force-balance BB, three-component Flat response velocity 33 mHz (30 s) to 50 Hz, others available Resolution: NLNM 25 mHz to 16 Hz (manufacturer) within 10 dB of NLNM within 20 dB of NLNM Operating range 10 mm/s Generator constant 2000 Vs/m, others available Output differential, 10 V per line Weight 9 kg Size 17 cm dia., 32 cm high Power 10 to 30 volts, 0.6 watts Manual control mass lock Remote control centering, mass lock optional Remote diagnostic mass position Accessories control and breakout box Typical installation all purpose. Submersible version is available Data sheet http://www.guralp.com/products/3ESP/ Remarks