Type Episensor ES-T Manufacturer Kinemetrics Inc. Address 222 Vista Avenue, Pasadena, CA 91107, USA Phone ++1 626 795 2220 E-mail sales@kmi.com Homepage www.kinemetrics.com Category Force-balance broadband accelerometer Flat response acceleration DC to 200 Hz Resolution: NLNM not applicable (this is a strong-motion instrument) within 10 dB of NLNM n.a. within 20 dB of NLNM n.a. Operating range user selectable, 0.25 g to 4 g Generator constant user selectable, order of 1 V s2 / m Output 2.5 volt single-ended to 20 volt differential Weight 2 kg Size 13 cm dia., 6 cm high Power 12 V or single 12 V, 0.15 to 0.4 W (depending on option) Manual control Centering; set gain Remote control - Remote diagnostic - Accessories - Typical installation Anywhere: Strong-motion monitoring, seismic zonation Data sheet http://www.kinemetrics.com/p-87-EpiSensor-ES-T.aspx Remarks This is a modern and popular strong-motion sensor. Its large dynamic range overlaps considerably with that of high-sensitivity seismometers, making it possible to record microearthquakes and teleseisms with this instrument.