Type S-13, GS-13 Manufacturer Geotech Instruments LLC Address 10755 Sanden Drive, Dallas, Texas 75238-1336, USA Phone (001) 214 221 0000 E-mail info@geoinstr.com Homepage www.geoinstr.com/ Category Electromagnetic single-component, short-period seismometer, convertible between horizontal and vertical Flat response velocity 1 Hz (adjustable) to >100 Hz Resolution: NLNM 0.07 to 40 Hz with low-noise preamplifier (S-13)* 0.05 to 150 Hz with low-noise preamplifier (GS-13)* within 10 dB of NLNM within 20 dB of NLNM above 0.04 Hz (GS-13)* Operating range large, limited by preamplifier Generator constant 630 Vs / m with 3600 Ohms coil (S-13) 2180 Vs / m with 3600 Ohms coil (GS-13) Output differential, unlimited Weight 14 kg. Moving mass is 5 kg. Size 17 cm dia., 38 cm high Power passive Manual control mass lock, centering, conversion Z / H Remote control calibration Remote diagnostic - Accessories - Typical installation observatory, short-period Data sheet http://www.geoinstr.com/ds-s13.pdf Remarks A widely used high-performance, short-period seismometer. For very quiet sites, Model GS-13 is the best choice. It resolves high-frequency signals much better than any broadband-feedback seismometer. See publications by Riedesel et al. (BSSA 80,6) and by Rodgers (BSSA 83,2 and 84,1) for information on preamplifier design and noise. * based on circuit analysis with op-amp LT1007 as a preamplifier. Low-noise model may be inaccurate above 10 Hz.