Type KS-2000 Manufacturer Geotech Instruments LLC Address 10755 Sanden Drive, Dallas, Texas 75238-1336, USA Phone (001) 214 221 0000 E-mail info@geoinstr.com Homepage www.geoinstr.com/ Category Force-balance, three-component, BB seismometer Flat response velocity 83 mHz to 50 Hz Resolution: NLNM 50 mHz to 15 Hz* within 10 dB of NLNM 35 mHz to 50 Hz* within 20 dB of NLNM 15 mHz to >100 Hz* Operating range 10 mm/s Generator constant 2000 Vs/m Output differential, 10 V per line Weight 11 kg Size 19 cm dia., 29 cm high Power 9 to 36 V, no current specified Manual control mass lock, centering (standard) Remote control mass lock, centering (M and borehole models), calibration Remote diagnostic mass position Accessories Typical installation Vault, field deployment Data sheet http://www.geoinstr.com/ds-ks2000m.pdf Remarks Based on the KS-54000 but smaller and about 20 dB noisier at low frequencies. Standard broadband response. Borehole and short-period versions are available. * based on Ringler and Hutt 2010. Resolution above 10 Hz is extrapolated.