Type KS-54000 Manufacturer Geotech Instruments LLC Address 10755 Sanden Drive, Dallas, Texas 75238-1336, USA Phone (001) 214 221 0000 E-mail info@geoinstr.com Homepage www.geoinstr.com/ Category Force-balance, three-component, VBB borehole seismometer Flat response velocity 0.003 Hz (330 s) to 5 Hz Resolution: NLNM 10 mHz to 5 Hz* within 10 dB of NLNM 4 mHz to 9 Hz* within 20 dB of NLNM 0.3 mHz to 12 Hz* Operating range 1 mm/s Generator constant 20000 Vs/m Output differential, 10 V per line Weight 66 kg Size 14 cm dia., 249 cm high Power 24 V, 2.4 W Manual control - Remote control mass lock, module leveling / centering, calibration Remote diagnostic mass position Accessories ancillary equipment for borehole deployment Typical installation borehole up to 300 m deep Data sheet http://www.geoinstr.com/ds-ks54000.pdf Remarks The standard borehole seismometer of the global network. Accepts up to 10 degrees borehole tilt. * based on Ringler and Hutt 2010.