Type REFTEK 151-120 “Observer” Manufacturer Refraction Technology, Inc. Address 1600, 10th Street, Suite A, Plano TX 75074, USA Phone ++1 214 440 1265 E-mail Info @ reftek.com Homepage http://www.reftek.com/ Category Force-balance VBB, three components Flat response Velocity 8.3 mHz (120 s) to 50 Hz Resolution: NLNM 8 mHz to 15 Hz* within 10 dB of NLNM 3 mHz to 30 Hz* within 20 dB of NLNM 0.4 mHz to 50 Hz* Operating range ±10 mm/s Generator constant 2000 Vs/m Output differential, 10 V per line Weight 12 kg Size 24 cm dia., 27 cm high Power 9 to 18 volts, 1.3 watts Manual control mass lock Remote control centering Remote diagnostic mass position Accessories Typical installation observatory, vault Data Sheet http://www.reftek.com/pdf/151-120.pdf Remarks A very good VBB sensor, in the free-mode band comparable to KS-1 and CMG-3TB according to Ringler & Hutt, 2010. * based on Ringler and Hutt 2010. Resolution above 10 Hz is extrapolated.