Type STS-1 VBB (out of production, see remarks below) Manufacturer Streckeisen AG Address Dättlikoner Str. 5, CH-8422 Pfungen, Switzerland Phone ++41 52 315 2161 E-mail none Homepage none Category Force-balance VBB, separate Z and H components Flat response velocity 2.67 mHz (360 sec) to 10 Hz Resolution: NLNM originally <0.3 mHz to 3 Hz, later versions up to 8 Hz* within 10 dB of NLNM 0.1 mHz to 13 Hz* within 20 dB of NLNM <0.1 mHz to 20 Hz* Operating range 8 mm/s Generator constant 2400 Vs/m Output differential, ±10 V per line Weight 4 kg (vert.); 5.5 kg (hor.) Size 12 * 17 * 18 cm (vert.); 20 cm dia. and 16 cm high (hor.) Shields require a space of 50 * 50 cm, 60 cm high. Power 15 volts, 3.5 watts per component Manual control mass lock (pins and screws inserted by hand) Remote control mass centering, calibration Remote diagnostic mass position Accessories feedback electronics are separate. Magnetic shield (for vert. comp. only), aluminum shield, glass base plate, vacuum glass bell included. Monitor (breakout) box optional. Typical installation observatory Data sheet www.software-for-seismometry.de/textfiles/Seismometry/ Remarks Operated under partial vacuum; no electronics inside the sensor. This seismometer made the very-broad-band velocity response popular, and is the only seismometer to resolve minimum ground noise throughout the long-period seismic band. (Some say it defines the low-noise model.) The STS1 is no longer manufactured by Streckeisen AG but Metrozet LLC (USA) have developed a modern, remotely controllable replacement for the feedback electronics and a modified mechanical sensor. The new system has the excellent low-frequency resolution of the original STS-1 but is easier to install and maintain. * based on Ringler and Hutt 2010. Resolution above 10 Hz is extrapolated.