Type STS 2.5 Manufacturer Streckeisen GmbH; exclusively sold by Quanterra, USA Address St: Dättlikoner Str. 5, CH-8422 Pfungen, Switzerland Q: 325 Ayer Rd, Harvard, Ma. 01451, USA Phone ++41 52 315 6700 (Streckeisen) ++1 978 772 4774 (Quanterra) E-mail bkemp@quanterra.com Homepage www.quanterra.com; www.kinemetrics.com/p-163-Home.aspx Category Force-balance VBB, symmetric-triaxial Flat response velocity 8.33 mHz (120 sec) to 50 Hz Resolution: NLNM 3 mHz to 20 Hz 3 within 10 dB of NLNM 0.3 mHz to 35 Hz 3 within 20 dB of NLNM 0.1 mHz to 50 Hz 3 Operating range ±13 mm/s Generator constant 1500 Vs/m Output differential, ±10 volts per line Weight 12 kg Size 23 cm dia., 26 cm high Power 9 to 28 volts, 0.5 watts Manual control - Remote control mass lock, centering, calibration, short-period mode Remote diagnostic mass position, state-of health parameters including temperature, internal humidity, tilt, serial number, supply voltage Accessories a “Host Box” with power conditioning and LED status indicators is included. Typical installation Observatory, vault. Needs additional protection in humid or dirty environments. Data Sheet http://www.kinemetrics.com/uploads/PDFs/STS-2_5.pdf Remarks Tightly-fitting thermal isolation required for optimum performance. The STS 2.5 has the same housing as the STS-2 but completely redesigned mechanical sensors and electronics. Remote control with a laptop computer. The STS 2.5 has not yet been extensively tested but appears to perform equally or slightly better than a third-generation STS-2. 3 self-noise data are from a third-generation, high-gain STS2, based on Ringler and Hutt 2010. Resolution above 10 Hz is extrapolated.