Type Trillium 240 Manufacturer Nanometrics Inc. Address 250 Herzberg Road, Kanata, Ontario, Canada K2K 2A1 Phone ++1 613 592 6776 E-mail info@nanometrics.ca Homepage http://www.nanometrics.ca/ Category Force-balance VBB, symmetric-triaxial Flat response velocity 41.7 mHz (240 s) to 35 Hz Resolution: NLNM 10 mHz to 10 Hz* within 10 dB of NLNM 0.3 mHz to 20 Hz* within 20 dB of NLNM 0.1 mHz to 35 Hz* Operating range ± 16 mm/s Generator constant 1200 Vs/m Output differential, ±10 volts per line Weight 14 kg Size 25 cm dia., 29 cm high Power 9 to 36 volt, 0.65 watt Manual control none: no mass lock required Remote control integrated web browser with many control options Remote diagnostic Mass positions, temperature, serial number, status, calibration parameters Accessories prefabricated heat shield Typical installation observatory, vault. Data sheet http://www.nanometrics.ca/products/trillium-240 Remarks An excellent very-broad-band seismometer, comparable to the STS2 in its performance. May be slightly better than the STS2 at the lowest frequencies when magnetically shielded. Has a modern digital control interface. * based on Ringler and Hutt 2010 and the manufacturer